## 6 – Worksheets

### Example worksheets

Worksheet 6-1: Environmental evaluation of the most important products and services

Company: Cheers Beers Ltd	Period: 2002

| Product name: Cleaning agent A | Little env. friendly | Very environmentally friendly | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Hazardous ingredients | X |  |  |  |  | 1 |
| Pollutants, air |  |  |  |  |  | n.c. |
| Pollutants, wastewater |  | X |  |  |  | 2 |
| Pollutants, soil |  | X |  |  |  | 2 |
| Raw materials |  |  |  |  |  | n.c. |
| Utilization of waste material |  |  |  |  |  | - |
| Packaging |  |  |  |  | X | 5 |
| Service life/shelf life |  |  |  |  |  | n.a. |
| Easy to repair |  |  |  |  |  | n.a. |
| Returnable |  |  | X |  |  | 3 |
| Energy consumption |  |  |  |  |  | n.c. |
| Water consumption |  | X |  |  |  | 2 |
| Recycling possibilities |  |  |  |  |  | n.a. |

n.c.: not considered; n.a.: not applicable

| Product name: Cleaning agent A | Little env. friendly | Very environmentally friendly | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Noise pollution |  |  |  |  |  | n.a. |
| Product declaration covers health protection and protection of the environment | X |  |  |  |  | 1 |
| Special training for operators required |  | X |  |  |  | 2 |
| Eco-label/quality label |  |  |  |  |  | - |
| Additional criteria and information |  |  |  |  |  |  |
| Total: | 18 |

n.c.: not considered; n.a.: not applicable

Worksheet 6-2: Evaluation of suppliers

Company: Cheers Beers Ltd	Period: 2002

| Name of the supplier: Detergent Company Cleaner | Does not meet requirements | Meets requirements | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Site certification of the supplier (ISO 14001/EMAS) |  |  |  |  | X | 5 |
| Information on product and material properties |  |  |  | X |  | 4 |
| Consultancy on environmental aspects of the products |  |  |  | X |  | 4 |
| Suggestions of environmentally friendly alternatives |  |  |  | X |  | 4 |
| Product range includes environmentally friendly products |  |  |  |  |  | n.a |
| Use of multi-way systems |  | X |  |  |  | 2 |
| Multi-way packaging material |  | X |  |  |  | 2 |
| Environmentally friendly transport |  |  |  | X |  | 4 |
| Supplier from the region |  |  |  |  | X | 5 |
| Customer service |  |  | X |  |  | 3 |
| Price |  |  | X |  |  | 3 |
| Total: | 36 |

n.c.: not considered; n.a.: not applicable

Worksheet 6-3: Register of hazardous materials

Company: The Cheers Beers Ltd.	Period: 2002

| No. | SDS. | Product name | Use | Hazardous ingredient(s) | Classification according to GHS | Container volume | Maximum of quantity stored | Storage area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ( | Hydrochloric acid T.S. 30 | Cleaning agent | Hydrogen chloride | C | 200 l barrel | 800 l | GL1 |
| 2 | ( | Cleaning agent A | Tank cleaning | Sodium hydroxide | C | 200 l barrel | 1,000 l | GL1 |
| 3 | ( | Cleaning agent B | Cleaning agent | Sodium hydroxide Potassium hydroxide | C | 200 l barrel | 400 l | GL1 |
| 4 | ( | Peracetic acid product Divosan forte | Disinfectant | Peracetic acid Hydrogen peroxide Acetic acid | O, C | 25 l canister | 100 l | GL1 |
| 5 | ( | Disinfectant A | Disinfectant | Bromacetic acid Phosphoric acid | C | 200 l barrel | 400 l | GL1 |
| 6 | ( | Disinfectant B | Disinfectant | Sodium hypochlorite | C | 200 l barrel | 400 l | GL1 |
| 7 | ( | Caustic soda 50% | Cleaning agent | Sodium hydroxide | C | 1 m3 container | 3,000 l | GL1 |
| 8 | ( | Gleitoklar | Chain lubricant | Isopropanol | Xi | 25 l canister | 75 l | GL1 |

Worksheet 6-4: Evaluation of risk potential, definition of measures

Company: Cheers Beers Ltd	Period: 2002

| Workplace: Fermenting tank | Product(s): P3 Ultrasil (cleaning agent C) |
| --- | --- |
| Department: Fermentation/brew house | Hazardous substances: sodium hydroxide, sodium hypochlorite |
| Responsible: F. Müller | Material number: 9 |
| Potential risks: | Causticity of the substance; possible release of chlorine gas in case of contact with an acid |
| Possible consequences: | Employees: Burning of skin, eyes and mucous membranes; intoxication if exposed to chlorine gas Plant/equipment/machinery: Possible chlorine induced corrosion Environment: Contamination of the environment or wastewater with hypochlorite solution |
| 1. Dangerous procedures/behaviour: | Risk | Probability |
| a) Skin contact or ingestion | Danger | Improb-able | Possible | Frequent |
| b) Accidental mixing of the product with acids | Minor | A |  |  |
|  | Medium |  | B |  |
| 2. Available safety precautions: | High |  |  | C |
| Protective clothing (gloves, protective jacket, protective boots) for employees 3. Options to improve the situation, proposed measures: Testing of alternative substances without chlorine Ensuring that the fermenting tank is not treated with acids at the same time Checking whether suitable protective clothing is used; contact the manufacturer of protective clothing | A . . . Situation acceptable B . . . Situation could be improved C . . . Action urgently required |

### Empty worksheets

Worksheet 6-1: Environmental evaluation of the most important products and services

Company:	Period:

| Product name: …………………………. | Little env. friendly | Very environmentally friendly | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Hazardous ingredients |  |  |  |  |  |  |
| Pollutants, air |  |  |  |  |  |  |
| Pollutants, wastewater |  |  |  |  |  |  |
| Pollutants, soil |  |  |  |  |  |  |
| Raw materials |  |  |  |  |  |  |
| Utilization of waste material |  |  |  |  |  |  |
| Packaging |  |  |  |  |  |  |
| Service life/shelf life |  |  |  |  |  |  |
| Easy to repair |  |  |  |  |  |  |
| Returnable |  |  |  |  |  |  |
| Energy consumption |  |  |  |  |  |  |
| Water consumption |  |  |  |  |  |  |
| Recycling possibilities |  |  |  |  |  |  |

n.c.: not considered; n.a.: not applicable

| Product name: ……………………………. | Little env. friendly | Very environmentally friendly | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Noise pollution |  |  |  |  |  |  |
| Product declaration covers health protection and protection of the environment |  |  |  |  |  |  |
| Special training for operators required |  |  |  |  |  |  |
| Eco-label/quality label |  |  |  |  |  |  |
| Additional criteria and information |  |  |  |  |  |  |
| Total: |  |

n.c.: not considered; n.a.: not applicable

Worksheet 6-2: Evaluation of suppliers

Company:	Period:

| Name of the supplier | Does not meet requirements | Meets requirements | Points |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 | 5 |  |
| Site certification of the supplier (ISO 14001/EMAS) |  |  |  |  |  |  |
| Information on product and material properties |  |  |  |  |  |  |
| Consultancy on environmental aspects of the products |  |  |  |  |  |  |
| Suggestions on environmentally friendly alternatives |  |  |  |  |  |  |
| Product range includes environmentally friendly products |  |  |  |  |  |  |
| Use of multi-way systems |  |  |  |  |  |  |
| Multi-way packaging material |  |  |  |  |  |  |
| Environmentally friendly transport |  |  |  |  |  |  |
| Supplier from the region |  |  |  |  |  |  |
| Customer service |  |  |  |  |  |  |
| Price |  |  |  |  |  |  |
| Total: |  |

n.c.: not considered; n.a.: not applicable

Worksheet 6-3: Register of hazardous materials

Company:	Period:

| No. | SDS. | Product name | Use | Hazardous ingredient(s) | Classification according to GHS | Container volume | Maximum of quantity stored | Storage area |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |

Worksheet 6-4: Evaluation of risk potential, definition of measures

Company:	Period:

| Workplace: | Product(s): |
| --- | --- |
| Department: | Hazardous substances: |
| Responsible: | Material number: |
| Potential risks: |  |
| Possible consequences: | Employees: Plant/equipment/machinery: Environment: |
| 1. Dangerous situation/behaviour: | Risk | Probability |
|  | Danger | Improb-able | Possible | Frequent |
|  | Minor | A |  |  |
|  | Medium |  | B |  |
| 2. Available safety precautions: | High |  |  | C |
| 3. Options to improve the situation, proposed measures: | A . . . Situation acceptable B . . . Situation could be improved C . . . Action urgently required |

Worksheet 6-5: Risk assessment sheet

Documentation of risk assessment

Basic information: company name and address, name of the workplace for which the assessment has been carried out, name(s) of person(s) working at the workplace, date of the assessment and the name(s) of person(s) conducting the assessment.

Record identified hazards in column 2 of the RISK ASSESSMENT SHEET.

For each identified hazard:

• Record classification according to GHS in column 3;

• Record preventive/protective measures used to limit the risks arising from a hazard in column 4;

• Record the results of risk assessment (e. g., high/unacceptable) in column 5;

• Record actions planned to reduce the risks in column 6.

Worksheet 6-5: Risk assessment sheet

|  | Date: _________________ |
| --- | --- |
| Company name and address: | Risk assessment carried out by: |
| Workplace (designation of the workplace): | Name of employee (name of person working at the workplace): |
| No. | Hazard | Classification | Prevention/protective measures used | Risk estimation/ evaluation | Actions planned to reduce risk |
| 1 | 2 | 3 | 4 | 5 | 6 |

# Footnotes

SDS = safety data sheet

SDS = safety data sheet